## Slide 1
India Air Quality
Analysis Project
Pollution Monitoring Across 31 States · 268 Cities · 7 Pollutants
3,197
Records
29
States
262
Cities
7
Pollutants
Source: Real-Time Air Quality Monitoring Stations · India

## Slide 2
PROJECT OVERVIEW
01
Load & Clean Data
Read CSV, parse dates, drop nulls, verify 3,197 clean records
02
Exploratory Analysis
5 objectives covering pollutants, states, cities & correlations
03
Visualisations
Bar charts, heatmap, scatter plot — one visual per objective
04
Linear Regression
Predict PM2.5 avg from min; 80/20 train-test split + CV
05
Model Validation
Per-pollutant R² check — CO, SO2, OZONE best performers

## Slide 3
PHASE 1 · Load & Clean Data
Raw Records
3,443
After Cleaning
3,197
States
29
Cities
262
Pollutants
7
Dataset Columns
Column | Type | Description
country / state / city | str | Geographic hierarchy
station | str | Monitoring station name
last_update | datetime | Timestamp (DD-MM-YYYY HH:MM)
latitude / longitude | float | Station coordinates
pollutant_id | str | CO, NH3, NO2, OZONE, PM10, PM2.5, SO2
pollutant_min/max/avg | int/float | Measured concentration values
Key Cleaning Steps
1. Parse last_update with dayfirst=True 2. Drop rows with null pollutant values (246 rows removed) 3. Convert all numeric columns with errors='coerce' 4. Reset index after cleaning

## Slide 4
OBJECTIVE 1 · National Average Pollution Level per Pollutant
Chart: 
| PM10 | PM2.5 | CO | NO2 | OZONE | SO2 | NH3
Avg Level | 96.49 | 78.65 | 38.85 | 29.98 | 21.77 | 16.27 | 6.29
Key Insights
PM10 is the most dangerous — avg 96.5 µg/m³, nearly 2× WHO limits
PM2.5 at 78.7 µg/m³ poses serious respiratory health risks
NH3 is lowest (6.3) — agricultural emissions relatively controlled
Particulate matter (PM) dominates pollution profile in India

## Slide 5
OBJECTIVE 2 · Most & Least Polluted States
Chart: 
| Delhi | Himachal Pradesh | Haryana | Uttar Pradesh | Madhya Pradesh | Punjab | Gujarat | Odisha | Rajasthan | Bihar
Avg Pollution | 73.9 | 64.86 | 50.01 | 46.95 | 46.94 | 46.49 | 43.6 | 40.33 | 39.21 | 39.2
🟢 Least Polluted States
State | Avg
Tripura | 8.6
Sikkim | 12.0
Puducherry | 16.4
Arunachal Pradesh | 18.0
Nagaland | 18.1
Delhi — #1 Most Polluted
73.9 µg/m³
average across all pollutants Driven by vehicle emissions, construction
dust, and industrial activity.

## Slide 6
OBJECTIVE 3 · Pollutant Spread — Min / Avg / Max
Chart: 
| PM2.5 | PM10 | OZONE | CO | NO2 | SO2 | NH3
Avg Min | 31.4 | 51.9 | 12.9 | 21.3 | 16.7 | 10.2 | 4.6
Avg Mean | 78.7 | 96.5 | 21.8 | 38.8 | 30 | 16.3 | 6.3
Avg Max | 158.8 | 172.7 | 66.1 | 65.4 | 52.1 | 27.5 | 9.1
Range = Max − Min
Pollutant | Range
PM2.5 | 127.4
PM10 | 120.8
OZONE | 53.2
CO | 44.1
NO2 | 35.4
SO2 | 17.3
NH3 | 4.5
PM2.5 and PM10 show the widest spread — highest variability across stations, indicating hotspot concentration zones.

## Slide 7
OBJECTIVE 4 · Top 10 Pollution Hotspot Cities
Chart: 
| Singrauli (MP) | Rupnagar (PB) | Nandesari (GJ) | Ramanagara (KA) | Greater Noida (UP) | Ghaziabad (UP) | Charkhi Dadri (HR) | Delhi (DL) | Bulandshahr (UP) | Mandideep (MP)
Avg Pollution | 111.67 | 100.25 | 94.5 | 89.2 | 82.93 | 79.5 | 74.67 | 73.9 | 73.71 | 70.14
City Spotlights
Singrauli
Madhya Pradesh
111.7
Heavy coal mining & thermal power plants
Rupnagar
Punjab
100.3
Industrial zone + crop burning
Nandesari
Gujarat
94.5
Chemical & pharmaceutical industries

## Slide 8
OBJECTIVE 5 · PM2.5 vs PM10 Correlation
Chart: 
| Chittoor | Araria | Arrah | Bettiah | Vijayawada | Motihari | Muzaffarpur | Anantapur | Rajamah. | Meerut
PM2.5 | 59 | 148 | 87 | 42 | 74 | 89 | 87 | 57 | 25 | 95
PM10 | 57 | 98 | 70 | 50 | 70 | 89 | 111 | 62 | 40 | 110
Pearson r =
0.60
Moderate Positive Correlation
Common Source:
Both PM types share emission sources — roads, construction, and industry
Not Identical:
r=0.60, not 1.0 — fine particles (PM2.5) behave differently from coarse (PM10)
Cities Covered:
3,764 city-level data points used for correlation analysis
Health Impact:
PM2.5 penetrates lungs deeper; PM10 affects upper respiratory tract

## Slide 9
PHASE 4 · Linear Regression — PM2.5 Min → PM2.5 Avg
Model Equation:
PM2.5_avg = 0.957 × PM2.5_min + 47.82
MAE
31.41
Avg prediction error
RMSE
43.84
Root mean sq error
R²
16.8%
Variance explained
CV R²
0.14
5-fold cross-val
PM2.5 Average Projections
PM2.5 Min | Projected Avg
10 | 57.4
20 | 67
30 | 76.5
40 | 86.1
50 | 95.7
60 | 105.2
100 | 143.5
150 | 191.4
Why is R² only 16.8%?
The low R² reflects real-world complexity. PM2.5 averages depend on wind, weather,
traffic, and industrial activity — not just the minimum reading. The model still captures
a statistically significant trend: every 1 unit rise in PM2.5 min raises the avg by ~0.96.
Phase 5 shows this model works far better for CO, SO2, and OZONE.

## Slide 10
PHASE 5 · Model Validation — Per-Pollutant R² Comparison
Chart: 
| CO | NH3 | NO2 | OZONE | PM10 | PM2.5 | SO2
R² Score | 0.6746 | 0.5524 | 0.6598 | 0.6703 | 0.4687 | 0.1677 | 0.6924
Full Validation Results
Pollutant | R² | MAE
CO | 0.67 | 10.89
NH3 | 0.55 | 1.55
NO2 | 0.66 | 9.71
OZONE | 0.67 | 6.92
PM10 | 0.47 | 25.34
PM2.5 | 0.17 | 31.41
SO2 | 0.69 | 5.22
R² ≥ 0.65 — Good fit
R² 0.50–0.65 — Acceptable
R² < 0.50 — Weak fit
SO2, CO & OZONE best predicted by this model ✓

## Slide 11
Conclusions & Takeaways
01
PM Pollution Dominates
PM10 (96.5) and PM2.5 (78.7) are India's most severe pollutants, far exceeding WHO guidelines across states.
02
Northern States at Risk
Delhi, Haryana, and UP face critically high pollution levels — urgent policy action needed in the Indo-Gangetic Plain.
03
Industrial Hotspots Identified
Singrauli, Rupnagar, and Nandesari are extreme hotspots driven by coal, chemicals, and heavy industry.
04
Moderate PM Correlation
PM2.5 and PM10 share common emission sources (r=0.60), but diverge enough to require separate policy treatment.
05
Regression Model Insights
SO2, CO, and OZONE are well-predicted by min values (R²≈0.67). PM2.5 needs multi-variable modelling.
Thank You · India Air Quality Analysis Project